## Slide 1: Introduction to GPGPU Programming
Junqi Yin
National Institute for Computational Sciences
June 9, 2015

## Slide 2: Pnmath
Motivation
History
GPU architecture
GPU programming model
CUDA C
CUDA tools
Other useful GPU tools
Summary
References
Outline:
Notes: Here is outline of today’s talk. I will talk about following topics.

## Slide 3: Pnmath
Motivation (GPU):
High CPU load
  Physics, AI, network
Graphic demand
  Fast memory access
    Many lookups [ vertices, normal, textures, … ]
  High bandwidth usage
    A few GB/s needed in regular cases !
  Large number of flops
    Flops = Floating Point Operations [ ADD, MUL, SUB, … ]
    Illustration: matrix-vector products
      (16 MUL + 12 ADD) x (#vertices + #normals) x fps =
      (28 Flops) x (6.000.000) x 30 ≈ 5GFlops
Conclusion: Real time graphics needs supporting hardware!
Notes: First let’s talk about why did we need GPU at all ? Then we will talk about how GPU can be useful for scientific computing.

## Slide 4: Pnmath
GPU: Graphics Processing Unit
  Designed to rapidly manipulate and alter memory in such a way so as to accelerate the building of images in a frame buffer intended for output to a display.
  The term was popularized by NVIDIA in 1999.
History:
Notes: GeForce 256 as "the world's first 'GPU', or Graphics Processing Unit, a single-chip processor with integrated transform, lighting, triangle setup/clipping, and rendering engines that is capable of processing a minimum of 10 million polygons per second".
ATI Technologies coined the term visual processing unit or VPU with the release of the Radeon 9700 in 2002.

## Slide 5: Pnmath
History of Graphics Hardware:
…-mid ’ 90s
  SGI mainframes and workstations
  PC: only 2D graphics hardware
mid’ 90s
  Consumer 3D graphics hardware (PC)
    3dfx, NVIDIA, Matrox, ATI, …
  Triangles rasterization (only)
1999
  PC-card with TnL (Transform and Lighting) … ]
    NVIDIA GeForce: Graphics Processing Unit (GPU)
  PC-card more powerful than specialized workstations
Modern graphics hardware
  Graphics pipeline partly programmable
  Leaders: NVIDIA and AMD
  Game consoles similar to GPUs(Xbox, Wii and Playstation)
Notes: What is Triangles rasterization ??
Wha it TnL (Transform and Lighting) ?

## Slide 6: Pnmath
General Purpose computation using GPU in applications other than 3D graphics
  GPU accelerates critical path of application
Data parallel algorithms leverage GPU attributes
  Large data arrays, streaming throughput
  Fine-grain SIMD parallelism
  Low-latency floating point (FP) computation
Applications – see //GPGPU.org
  Game effects (FX) physics, image processing
  Physical modeling, computational engineering, matrix algebra, convolution, correlation, sorting
What is GPGPU:

## Slide 7: Pnmath
Motivation (GPGPU):
Computation
Memory

## Slide 8: Pnmath
Modern GPUs are very efficient at
  Manipulating computer graphics, and their highly parallel structure makes them more effective than general-purpose CPUs for algorithms where processing of large block of data is done in parallel.
GPUs are massively multithreaded manycore chips.
  NVIDIA tesla products have upto 512 cores.
  Over 665 GFLOPS sustained performance (double precision floating point)
  6GB of Memory
  Memory bandwidth upto 177 GBytes/sec.
Users across science and engineering disciplines are achieving very good speedups on GPUs.
GPU continue:
Notes: Tesla M2090
Peak Double precision 665 Gigaflops (Tesla M2090)
Peak Single precision 1331 Gigaflops (Tesla M2090)
Memory bandwidth  177 GBytes/sec (internal)
Memory size => 6GB
512 CUDA cores
Users across science & engineering disciplines are achieving 100x or better speedups on GPUs

## Slide 9: Pnmath
Desktop GPUs
  GeForce series for CPU
Mobile GPUs
  GeForce series for Mobile
Workstation GPUs
  Quadro NVS, Tesla
NVIDIA GPUs:

## Slide 10: Pnmath
Supports CUDA and OpenCL
Fermi(Tesla version)
  Upto 512 cores
  Upto 6GB memory
  Upto 665 GFLOPS – Double precision
  Caches included: L1 per multiprocessor, L2 shared
Kepler in 2012
Maxwell in 2014
NVIDIA GPUs:

## Slide 11: Pnmath
Desktop GPUs
  Radeon series
Mobile GPUs
  Mobility Radeon
Workstation GPUs
  FirePro, FireStream
Supports OpenCL (no CUDA)
AMD GPUs:

## Slide 12: Pnmath
Large amount of nodes.
  Distributed memory
  Multicore processors (e.g. 12 cores per node Kraken)
Fast interconnect.
Programming models
  MPI
  Hybrid (Pthreads/OpenMP with MPI)
Typical Supercomputer:

## Slide 13: Pnmath
Accelerated HPC floating workloads using GPUs.
  Peak FP performance 10x vs CPU.
  Memory bandwidth 20x vs CPU.
  Parallelism, of the order of 500 cores, thousands of threads.
GPUs are accelerators.
  Has its own fast memory.
  Separate card connected to CPU node Via PCI-E bus.
Accelerated Supercomputer:
Notes: Peripheral Component Interconnect Express: PCI Express is used in consumer, server, and industrial applications, as a motherboard-level interconnect (to link motherboard-mounted peripherals), a passive backplane interconnect and as an expansion card interface for add-in boards.

## Slide 14: Pnmath
Intel
  Intel MIC(Many Integrated Core)
  ~ 63 X86 vector cores
  OpenMP, OpenCL, Intel parallel building blocks etc...
  First commercial product(Knights corner) in 2012.
Other(FPGA and DSP based system etc…)
Other accelerators:
Reference: http://intel.com

## Slide 15: Pnmath
SIMD(Single Program, Multiple Data) are best.
Operations need to be sufficient size to overcome overhead of memory transfer.
Think millions of operations.
*Not* for all applications:

## Slide 16: Pnmath
GPU is specialized for compute-intensive, highly parallel computation-exactly what graphics rendering is about.
GPU devotes more transistors to data processing rather than data caching and flow control.
How it is different from CPU:
Notes: The reason behind the discrepancy in floating-point capability between the CPU and the GPU is that the GPU is specialized for compute-intensive, highly parallel computation – exactly what graphics rendering is about – and therefore designed such that more transistors are devoted to data processing rather than data caching and flow control, as schematically illustrated by Figure 1-2.
I will talk about Memory Hierchcy in detail .

## Slide 17: Pnmath
The GPU is viewed as a compute device that.
  Is a coprocessor to the CPU or host
  Has its own device memory
  Runs many threads in parallel
Data-parallel portions of an application are executed on the device as kernels which run in parallel on many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight (Very little creation overhead)
  GPU needs 1000s of threads for full efficiency(Multi-core CPU needs only a few)
More on GPU:

## Slide 18: Pnmath
Trying it together:

## Slide 19: Pnmath
GPU architecture :
Reference: http://nvidia.com
Streaming Multiprocessors (SMs)
32 cores
Notes: High level block diagram of NVIDIA GPU chip :
NVIDIA’s Fermi GPU architecture consists of multiple streaming multiprocessors (SMs), each consisting of 32 cores, each of which can execute one floating point or integer instruction per clock.
The SMs are supported by a second-level cache, hostinterface, GigaThread scheduler, and multiple DRAM interfaces.
The 512 CUDA cores are organized in 16 SMs of 32 cores each.
A Raster Opterator - basically, they're the final stage of pushing pixels to your screen. Larger numbers of these are fairly unimportant compared to other pipelines, since they spend a lot of their time idle waiting for pixels to push.
Raster Operation Unit

## Slide 20: Pnmath
Multilevel levels of memory hierarchy
Reference: http://nvidia.com
GPU architecture :
Notes: If we zoom in one of the SM it looks like this.
Where PE=processing elements
ROP = Raster operators.

## Slide 21: Pnmath
Thread: is a ready for execution/running instance of a kernel. Each thread has its own instruction address counter and register state.
Warp: is a group of 32 parallel threads.
Block: is a groups of Warps. A block is executed on one multiprocessor. Every block has its own shared memory and registers in the multiprocessor.
Grid: is a group of Blocks.
Host: is the CPU in CUDA applications.
Device: is the GPU in CUDA applications.
Terminology:
Notes: Thread: is a ready-for-execution/running instance of a kernel. Each thread has its own instruction address counter and register state. Each thread can be identified by a combination of its three-dimensional thread index and three-dimensional thread-block index. CUDA threads are lightweight. This means that creating and destroying a thread is very fast.
Warp: is a group of 32 parallel threads. The multiprocessors create and execute warps in order. All threads in a warp start together but each of them can have its own instruction and registers.
Block: is a group of Warps. A block is executed on one multiprocessor. Every block has its own shared memory and registers in the multiprocessor.
Grid: is a group of blocks. There should be at least as many blocks as multiprocessors (and preferably at least 2× as many).
Host: is the CPU in CUDA applications.
Device: is the GPU in CUDA applications.

## Slide 22: Pnmath
A device has a set of multiprocessors
Each multiprocessors is a set of 32-bit processors with Single Instruction Multiple Data architecture.
At each clock cycle, a multiprocessor executes the same instruction on a group of threads called warp.
The number of threads in a warp is the warp size.
A set of SIMD multiprocessors:
Reference: http://nvidia.com
Device
Multiprocessor N
Multiprocessor 2
Multiprocessor 1
Instruction
Unit
Processor 1
…
Processor 2
Processor M
Notes: Register per thread (faster than local memory)
Local memory : per thread
Shared memory : per block (all threads in block can access it)
Global memory : shared with all blocks + accessible by host not cached
Constant memory : shared with all block + accessible by host cached (There is a total of 64 KB constant memory on a device.) Read only by threads. Host can write it.
Texture memory : shared with all block + accessible by host cached. Read only by threads. Host can write it.

## Slide 23: Pnmath
SIMD Execution of warpsize=M threads (from single block)
  Result is a set of instructions streams roughly equal to # of blocks in threads divided by warpsize.
Multithreaded Execution across different instruction streams within block.
  Also possibly across different blocks if there are more blocks than SMs(streaming multiprocessors)
Each block mapped to single SM
  No direct interaction across SMs
Hardware Execution Model:
Reference: http://nvidia.com
Device
Multiprocessor N
Multiprocessor 2
Multiprocessor 1
Device memory
Shared Memory
Instruction
Unit
Processor 1
Registers
…
Processor 2
Registers
Processor M
Registers
Constant
Cache
Texture
Cache
Notes: Register per thread (faster than local memory)
Local memory : per thread
Shared memory : per block (all threads in block can access it)
Global memory : shared with all blocks + accessible by host not cached
Constant memory : shared with all block + accessible by host cached (There is a total of 64 KB constant memory on a device.) Read only by threads. Host can write it.
Texture memory : shared with all block + accessible by host cached. Read only by threads. Host can write it.

## Slide 24: Pnmath
GPU has much more aggressive memory subsystem
The local, global, constant and texture spaces are regions of device memory.
Each multiprocessor has:
  A set of 32-bit registers per processors
  On chip shared memory
  A read-only constant cache (To speed up access to the constant memory space)
  A read-only texture cache
  (To speed up access to the texture memory space)
Memory Model:
Reference: http://nvidia.com
Device
Multiprocessor N
Multiprocessor 2
Multiprocessor 1
Device memory
Shared Memory
Instruction
Unit
Processor 1
Registers
…
Processor 2
Registers
Processor M
Registers
Constant
Cache
Texture
Cache
Global, constant, texture memories
Notes: Register per thread (faster than local memory)
Local memory : per thread
Shared memory : per block (all threads in block can access it)
Global memory : shared with all blocks + accessible by host not cached
Constant memory : shared with all block + accessible by host cached (There is a total of 64 KB constant memory on a device.) Read only by threads. Host can write it.
Texture memory : shared with all block + accessible by host cached. Read only by threads. Host can write it.

## Slide 25: Pnmath
Each thread can:
  Read/write per-thread registers
  Read/write per-thread local memory
  Read/write per-block shared memory
  Read/write per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
The host can read/write global/constant, and texture memory
GPU memory model:
Reference: http://nvidia.com
Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: Register per thread (faster than local memory)
Local memory : per thread
Shared memory : per block (all threads in block can access it)
Global memory : shared with all blocks + accessible by host not cached
Constant memory : shared with all block + accessible by host cached (There is a total of 64 KB constant memory on a device.) Read only by threads. Host can write it.
Texture memory : shared with all block + accessible by host cached. Read only by threads. Host can write it.

## Slide 26: Pnmath
How to use GPUs
Use existing GPU software
Use available libraries for GPUs
Program GPU with directives
Program native GPU code
GPU programming:
EFFORT
Low
High
Notes: Applications => NWCHEM, GROMACS, HMMER,
E.g.  Numerical libraries (MAGAM, CULA, CUFFT, CUBLAS )
GPU directives => OpenACC, HMPP and OpeMP 4.0
Native code => Using CUDA and OpenCL

## Slide 27: Pnmath
NAMD, GROMACS, GPU-HMMER, TeraChem
Pros
  No implementation headaches for end users.
Cons
  Existing applications do not cover all science areas.
  Often include limited number of algorithms/models.
  For many applications the GPU version is still immature.
Use existing GPU software:
Notes: Existing applications do not cover all science areas
• Often include limited number of algorithms/models
• For many applications the GPU version is still immature

## Slide 28: Pnmath
GPU accelerator is called device, CPU is host.
GPU code (kernel) is launched and executed on the device by several threads.
Threads grouped into thread blocks.
Program code is written from single thread's point of view.
  Each thread can diverge and execute a unique code path (can cause performance issues )
GPU programming model:
Notes: Divergence
– Threads in a warp take different execution paths
Reason: Control Flows in Code
– E.g., if, do, for, while, switch
• Input Data Dependence
– Input data-set --> execution path
– Thread-data mapping --> amount of thread divergence
Effect: It Degradis GPU Throughput

## Slide 29: Pnmath
A kernel is executed as a grid of thread blocks
  All threads share data memory space
A thread block is a batch of threads that can cooperate with each other by:
  Synchronizing their execution
  Efficiently sharing data through a low latency shared memory
Two threads from two different blocks cannot cooperate
Thread Batching: Grids and Blocks
Reference: http://nvidia.com
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 30: Pnmath
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D (blockIdx.x, blockIdx.y)
  Thread ID: 1D, 2D, or 3D (threadIdx.{x,y,z})
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
Block and Thread IDs
Reference: http://nvidia.com
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 31: Pnmath
Threads:
  3D IDs, unique in block
Blocks:
  2D IDs, unique in grid
Dimensions are set at kernel launch.
Built-in variables for device code:
  threadIdx, blockIdx
  blockDim, gridDim
Thread Hierarchy :
Notes: Built-in variables for device code:
– threadIdx, blockIdx – blockDim,gridDim

## Slide 32: Pnmath
Compute Unified Device Architecture
CUDA is a C/C++ language extension for GPU programming.
  PGI has developed similar FORTRAN 2003 extension.
Two APIs: Runtime and Driver
Introduction to CUDA:
Notes: You have to have Nvidia GPU, Driver and CUDA SDK (Latest is 5.0)

## Slide 33: Pnmath
CUDA applications:

## Slide 34: Pnmath
CUDA software stack:
Reference: http://nvidia.com
Notes: CUDA libraries
CUDA Runtime: NVCC and PTX
CUDA Driver
GPU

## Slide 35: Pnmath
Qualifiers
  global, device, shared, local, constant…
Built-in variables
  threadIdx, blockIdx
Intrinsics
  __syncthreads,
Runtime API
  Memory, device execution management.
Kernel launch
Introduction to CUDA C:
__device__ float array[128];
__global__ void kern(float *data){
__shared__ float buffer[32};
....
buffer[threadIdx.x] = data[i];
....
__syncthreads;
....
}
float *d_data;
cudaMalloc((void **))&d_data, bytes);
kern<<<1024, 128>>>(d_data);
Notes: You need to have basic knowledge of C/C++ to learn CUDA.
These are some basic C introduction, Not a complete list by any means.
__device__ float array[128]; __global__ void kern(float *data) { __shared__ float buffer[32]; ... buffer[threadIdx.x] = data[i]; ... __syncthreads; ... }
float *d_data; cudaMalloc((void**)&d_data, bytes); kern<<<1024, 128>>>(d_data);
__syncthreads, => Synchronizes in all thread of current block
Kernels designated by function qualifier:
__device__
Function called from device and run on device Cannot be called from host code
__global__
Function called from host and executed on device Must return void
Other CUDA function qualifiers
__host__
Function called from host and executed on host (default)
__host__ and __device__ qualifiers can be combined to generate both CPU and GPU code

## Slide 36: Pnmath
CUDA function declarations:
 | Executed on the: | Only callable from the:
__device__ float DeviceFunc() | device | device
__global__ void KernelFunc() | device | host
__host__ float HostFunc() | host | host

## Slide 37: Pnmath
Vector add CPU:
void add(int *a, int *b, int *c)
{
int i;
for (i=0; i<N; i++)
{
c[i] = a[i] + b[i];
}
}

## Slide 38: Pnmath
//include header files
#include <cuda.h> #include <cutil.h> //include kernels #Add "vector_add_kernel gpu code here" //next slide
static const int N = 100000;
int main( int argc, char** argv) {
int a[N], b[N], c[N];
int *dev_a, *dev_b, *dev_c;
//Memory allocation on device
cudaMalloc(&dev_a, N*sizeof(int);
cudaMalloc(&dev_b, N*sizeof(int);
cudaMalloc(&dev_c, N*sizeof(int);
//Memory copy host to device
cudaMemcpy(dev_a, a, N*sizeof(int), cudaMemcpuKind:cudaMemcpuHostToDevice);
cudaMemcpy(dev_b, b, N*sizeof(int), cudaMemcpuKind:cudaMemcpuHostToDevice);
//Call Kernel (in next slide)
//Copy result from GPU to CPU
cudaMemcpy(c,dev_c, N*sizeof(int), cudaMemcpuKind:cudaMemcpuDeviceToHost);
//Free memory
cudaFree(dev_a); cudaFree(dev_b); cudaFree(dev_c);
}
CUDA memory management:
// Initialize vectors on host
int p;
for( p = 0; p < n; p++ ) {
a[p] = sin(p)*sin(p);
b[p] = cos(p)*cos(p);
}
gpucode.cu
Notes: I allocate three Device vectors (dev_a, dev_b, dev_c). Then I copy the Host vectors (a, b) in the Device vectors (dev_a, dev_b).
CUDAMEMCOPY( dst - Destination memory address
src - Source memory address
count - Size in bytes to copy
kind - Type of transfer
)

## Slide 39: Pnmath
Vector launch kernel:
add<<<1,1>>>(dev_a, dev_b, dev_c);//serial
add<<<N/256,256>>>(dev_a, dev_b, dev_c);//parallel
//Number of blocks in grid = N/256 = gridSize
//Number of threads per block = 256 = blockSize
Notes: execute grid of N/256 blocks of 256 threads each block
vecAdd<<<N/256, 256>>>(d_A, d_B, d_C);

## Slide 40: Pnmath
//vector_add_kernel gpu code (serial)
static const int N=100000;
__global__ void add(int *a, int *b, int* c)
{
for(int i=0;i<N;i++){
c[i] = a[i] + b[i];
}
}
Vector add kernel function:
Notes: __global__” to say “this is a Device function callable from Host”.
A question… Is there any parallel code in this sample ? No, the code is iteratif. But if there is a for, the traitment could be parallelized ?

## Slide 41: Pnmath
//vector_add_kernel gpu parallel
__global__ void add(int *a, int *b, int* c)
{
int idx = threadIdx.x + blockDim.x * blockId.x;
c[idx] = a[idx] + b[idx];
}
Vector add kernel function:
Notes: blockIdx is one of the Cuda bult-in. It gives you the possibility to know the current block number.
Why is it blockIdx.x and not only blockIdx ? Because you can have a block collection (so two dimension).
Now your addition is executed on N blocks and every block does one addition.
We could represent this like that :
//c[blockIdx.x] = a[blockIdx.x] + b[blockIdx.x]
//int idx = threadIdx.x + blockDim.x * blockId.x;
// Get our global thread ID
int id = blockIdx.x*blockDim.x+threadIdx.x;
// Make sure we do not go out of bounds
if (id < n)
c[id] = a[id] + b[id];
int id = blockIdx.x*blockDim.x+threadIdx.x;

## Slide 42: Pnmath
Modified C function call syntax:
kernel<<<dim3 dG, dim3 dB>>>(...)
  Execution Configuration (“<<< >>>”)
  dG - dimension and size of grid in blocks Two-dimensional: x and y Blocks launched in the grid: dG.x * dG.y
  dB - dimension and size of blocks in threads: Three-dimensional: x, y, and z Threads per block: dB.x * dB.y * dB.z
  Unspecified dim3 fields initialize to 1
dim3 DimGrid(100, 50); // 5000 (# of thread blocks in grid (gridsize))
dim3 DimBlock(4, 8, 8); // 256 (# of threads per block (blocksize))
Launching Kernels:

## Slide 43: Pnmath
Kernel Launch:
The kernel is the heart of our CUDA code. When a kernel is launched the number of threads per block(blockDim) and number of blocks per grid(gridDim) are specified.
The total number of threads = (gridDim) * (blockDim)
Each thread evaluates one copy of the kernel.

## Slide 44: Pnmath
Compilation tools are a part of CUDA SDK.
nvcc compiler translates code written in CUDA into PTX.
nvcc separates the code for host and device.
  Host code is compiled with regular C/C++ compiler.
More information: http://www.nics.tennessee.edu/~ksharkey/tutorials/
https://www.olcf.ornl.gov/tutorials/cuda-vector-addition/
Compiling CUDA code:
Notes: nvcc‘ (nVidia gcc) compiler translates code written in CUDA into PTX
GPU contains a compiler which translates the PTX into something which can be run on the processing cores.
Parallel Thread Execution (PTX) is a pseudo-assembly language used in nVidia's CUDA programming environment.
Thank you Kevin, here you can find more information about how to compile cuda code on GPU

## Slide 45: Pnmath
More information: http://www.nics.tennessee.edu/~ksharkey/tutorials/
Compiling CUDA code:
On Keeneland:
>module load PE-intel
>module load cuda/4.1
> nvcc –ccbin $CC –o gpu.out gpucode.cu
On Nautilus:
>module load PE-gnu
>module load cuda/4.0RC2
> nvcc –ccbin $CC –o gpu.out gpucode.cu
Notes: ccbin = Specify the directory in which the compiler executable
nvcc -ccbin $CC -o dq.x dq.cu
You can find many different CUDA programs in CUDA SDK example: Vector addition, Matrix multiplication, MultiGPU program etc..

## Slide 46: Pnmath
More information: https://wiki-rdav.nics.tennessee.edu/index.php/Using_the_Nvidia_GPUs_on_Nautilus
AND
http://keeneland.gatech.edu/support/quick-start#runningjobs
Running CUDA code:
On Keeneland:
> qsub –I -l nodes=1:ppn=1:gpus=3,walltime=00:30:00
> ./gpu.out
On Nautilus:
> qsub –I –l ncpus=1,gpus=1,walltime=00:30:00
> ./gpu.out
Notes: You can submit batch job as well.

## Slide 47: Pnmath
CUDA with MultiGPU
CUDA + OpenMP
CUDA + MPI
CUDA + OpenMP + MPI
Hybrid programming:

## Slide 48: Pnmath
MAGMA
CUBLAS
CULA
CUFFT
CUSPARSE
THRUST
Optix
CUDA libraries:
Easy to use in your programs.
Algorithms in libraries are usually efficient.
Notes: Pros
– Easy to implement in your programs
– Algorithms in libraries are usually efficient • Cons
– Speedup limited by Amdahl’s law and there is still transfer bottleneck

## Slide 49: Pnmath
Debuggers:
  Allinea DDT
  CUDA-GDB
  Totalview
  Cuda-memcheck
Profilers:
  Tau
  NVIDIA visual profiler
CUDA debuggers and profilers:
Notes: cuda-memcheck
– Very helpful tool to find indexing or other memory related bugs

## Slide 50: Pnmath
NVIDIA: CUDA
Use compiler to build kernels
C language extensions(nvcc)
  Also a low-level driver-only API
CUDA and OpenCL:
Open-free standard.
Builds kernel at runtime.
API only, no new compiler-API calls to execute kernel
https:/www.khronos.org/opencl/
http://www.nvidia.com/object/cuda_home_new.html
Notes: API only; no new compiler – API calls to execute kernel
OpenCL is a free standard for cross-platform, parallel programming heterogeneous computing.
It is not only for GPU but for also for other architectures,

## Slide 51: Pnmath
Two main products
  PGI accelerators
  HMPP (CAPS enterprise)
Normal C or Fortran code with directives to guide compiler in creating a GPU version.
Backend supporting CUDA, OpenCL and even normal CPUs.
Directive based GPU code:

## Slide 52: Pnmath
Pros
  Same code base as CPU version
  Less time consuming
  Portability is better due to different back-ends support.
Cons
  Generated code may not be as fast as hand-tuned CUDA.
Directive based GPU code:

## Slide 53: Pnmath
A collection of compiler directives to specify loops and regions of code in standard C,C++ and Fortran.
Allow programmer to create high-level host+ accelerators programs without the need to explicitly initialize the device, manage data or program transfers.
Backed by PGI, CAPS, Cray and NVIDIA
Part of OpenMP 4.0 ?
More information: http://www.openacc-standard.org/
OpenACC:
Notes: The OpenACC Application Program Interface describes a collection of compiler directives to specify loops and regions of code in standard C, C++ and Fortran to be offloaded from a host CPU to an attached accelerator, providing portability across operating systems, host CPUs and accelerators.
The directives and programming model defined in this document allow programmers to create high-level host+accelerator programs without the need to explicitly initialize the accelerator, manage data or program transfers between the host and accelerator, or initiate accelerator startup and shutdown.
All of these details are implicit in the programming model and are managed by the OpenACC API-enabled compilers and runtimes. The programming model allows the programmer to augment information available to the compilers, including specification of data local to an accelerator, guidance on mapping of loops onto an accelerator, and similar performance-related details.

## Slide 54: Pnmath
Aim to compile CUDA programs to so that they can be run on architectures other than NIVIDA GPUs
It is a modular dynamic compilation framework for heterogeneous system, providing various backend targets for CUDA programs and analysis modules for the PTX virtual instruction set.
Proliferation of Heterogeneous computing.
Ocelot currently allows CUDA programs to be executed on NVIDIA GPUs, AMD GPUs, and x86-CPUs at full speed without recompilation.
Ocelot:
Notes: Ocelot is a modular dynamic compilation framework for heterogeneous system, providing various backend targets for CUDA programs and analysis modules for the PTX virtual instruction set.
Ocelot currently allows CUDA programs to be executed on NVIDIA GPUs, AMD GPUs, and x86-CPUs at full speed without recompilation.

## Slide 55: Pnmath
pyCUDA, pyOpenCL
MATLAB with CUDA toolbox
CUDA FORTRAN
ROpenCL, RCUDA
Haskell, Perl etc…
Programming languages and GPGPU:

## Slide 56: Pnmath
http://developer.nvidia.com/category/zone/cuda-zone
http://gpgpu.org/
http://developer.nvidia.com/about-parallel-forall
http://www.gputechconf.com/page/home.html#
http://software.intel.com/en-us/articles/vcsource-tools-opencl-sdk/
http://developer.amd.com/pages/default.aspx
http://developer.download.nvidia.com/compute/DevZone/docs/html/CUDALibraries/doc/CUBLAS_Library.pdf
http://www.vpac.org/files/GPU-Slides/04.debugging_profiling_tools.pdf
http://keeneland.gatech.edu/software/cuda
http://developer.nvidia.com/nvidia-visual-profiler
Resources:
Notes: If you are interested to look for latest update of GPGPU
Parallel Forall is NVIDIA’s GPU Computing developer blog, focused on providing detailed technical information on a variety of programming topics, including CUDA C/C++, OpenACC, GPU-accelerated libraries, GPU programming techniques, and much more.
GPU tech conference coming up : GPU Technology Conference
http://developer.amd.com/pages/default.aspx  OpenCL, APU FUSION development toolkit,
http://developer.download.nvidia.com/compute/DevZone/docs/html/CUDALibraries/doc/CUBLAS_Library.pdf

## Slide 57: Pnmath
Get the data on the GPU(and keep it there! If possible)
  PCIe x16 v2.0 bus: 8GiB/s in a single direction
  GPUs: ~180 GiB/s
Give the GPU enough work to do
Reuse and locate data to avoid global memory bottlenecks
Corollary: Avoid malloc/free
Rules for fast GPU code:
Notes: rules for fast GPU codes
Get the data on the GPU (and keep it there!)
  PCIe x16 v2.0 bus: 8 GiB/s in a single direction
  20-series GPUs: 140-200 GiB/s
Give the GPU enough work to do
  Assume 10 ms latency and 1 TF device
  Can waste (10-6 * 1012) = 1M operations
Reuse and locate data to avoid global memory bandwidth bottlenecks
  1012 flop hardware delivers 1010 flop when global memory limited
  Can cause a 100x slowdown!
  Corollary: Avoid malloc/free!

## Slide 58: Pnmath
Accelerated supercomputers are emerging.
GPUs offer tremendous potential to accelerate scientific applications.
Newer generations GPUs getting easier to program.
Challenges still remain in using them efficiently.
Still a few cliffs:
  HOST-GPU transfer
  Careful memory access
  Lots of parallelism
  Thread divergence
Summary:
Notes: Divergence
– Threads in a warp take different execution paths
Reason: Control Flows in Code
– E.g., if, do, for, while, switch
• Input Data Dependence
– Input data-set --> execution path
– Thread-data mapping --> amount of thread divergence
Effect: It Degradis GPU Throughput

## Slide 59: Pnmath
Challenges remain
  Applicability: Can you solve your algorithm efficiently using a GPU ?
  Programmability: Effort of code writing that uses a GPU efficiently.
  Portability: Incompatibilities between vendors
  Availability: Are you able gain access to large scale system ?
  Scalability: Can you scale the GPU software efficiently to several nodes ?
Accelerated Supercomputer:

## Slide 60: Pnmath
https://nimrodteam.org/meetings/team_mtg_8_10/nimrod_gpu.pdf
http://people.maths.ox.ac.uk/~gilesm/hpc/NVIDIA/NVIDIA_CUDA_Tutorial_No_NDA_Apr08.pdf
http://www.nvidia.com/docs/IO/105880/DS-Tesla-M-Class-Aug11.pdf
http://www.nics.tennessee.edu/~ksharkey/tutorials/
http://en.wikipedia.org/wiki/Graphics_processing_unit
http://www.cc.gatech.edu/~vetter/keeneland/tutorial-2012-02-20/08-opencl.pdf
http://developer.amd.com/gpu_assets/OpenCL_Parallel_Computing_for_CPUs_and_GPUs_201003.pdf
http://gamelab.epitech.eu/blogtech/?p=28
Introduction GPU computing by Sebastian von alfthan
Supercomputing for the Masses: Killer-Apps, Parallel Mappings, Scalability and Application Lifespan by Rob Farber
The PTX GPU Assembly Simulator and Interpreter By N.M. Stiffler, Zheming Jin, Ibrahim Savran
References:

## Slide 61: Pnmath
In this tutorial session, we covered
  GPU architecture
  GPU programming model
  CUDA C
  CUDA tools
  Other useful GPU tools
  References
Summary/Wrapping up:

## Slide 62: Pnmath
Thank You for attending NICS HPC Seminar Series !!!
Notes: Thank you very much for attending NICS-RDAV training. If you have any question, Please ask me or you can email me at pragnesh@utk.edu

## Slide 63: Pnmath
It combines the speed of CUDA and the graphics of the GPU with the user friendliness.
Provides GPU library for C, C++, Fortran, Python and MATLAB.
Provides GPU counterparts to CPU data types, such as real and complex double, single,uint32, int32, logical, etc. Any variable residing in the host (CPU) memory can be cast to Jacket's GPU data types.
It’s memory management system allocates and manages memory for these variables on the GPU automatically, behind-the-scenes. Any functions called on GPU data will execute on the GPU automatically without any extra programming.
For more information: http://www.accelereyes.com/
Jacket:
Notes: Here I am talking about MATLAB
Jacket's memory management system allocates and manages memory for these variables on the GPU automatically, behind-the-scenes. Any functions called on GPU data will execute on the GPU automatically without any extra programming.
addpath <jacket_root>/engine
X = gdouble( magic( 3 ) );
Y = gones( 3, 'double' );
A = X * Y

## Slide 64: Pnmath
CPU:
X = double( magic( 3 ) );
Y = ones( 3, 'double' );
A = X * Y
GPU:
addpath <jacket_root>/engine
X = gdouble( magic( 3 ) );
Y = gones( 3, 'double' );
A = X * Y
Jacket example:
Notes: Note that the only difference between this code and CPU-based MATLAB code is the introduction of the GDOUBLE casting functions and GONES. GONES is equivalent to the MATLAB ONES function but creates the matrix on the GPU.
Suppose you want to bring matrix A on CPU to do some CPU processing. We can use standard MATLAB casting "double(A)" to copy it on CPU memory.